## Slide 1
HP-WAN Documents Updates
(State-Of-Art I-D and Framework I-D)
Quan Xiong,
ZTE
IETF 124 @ Montreal HP-WAN Side meeting
November, 2025

## Slide 2: HP-WAN Quick Reminder
Scope: NRENs and large dedicated backbones supporting data-intensive science, distributed AI training, and HPC. Examples: GÉANT, ESnet, Janet, Internet2, CANARIE, CERNET.
Problem: Multi-petabyte data movement across distance needs high bandwidth, low latency, high reliability, and secure end-to-end design from campus to backbone (e.g., Science DMZ).
Key components: Distributed architectural elements, topology choices, bandwidth and latency engineering, localised data movement, forwarding optimisation, reliability/HA.
Data movement enablers: Scheduled low-latency hard guarantees, QoS, congestion control, performance monitoring, scalability.

## Slide 3: Two Important Documents
“Current State of the Art for High Performance Wide Area Networks”
  This document provides an overview of the terminology and techniques used for existing HP-WANs. It also explores the technological advancements, operational tools, and future directions for HP-WANs, emphasising their role in enabling cutting-edge scientific research, AI training and massive R&E data analysis.
  https://datatracker.ietf.org/doc/html/draft-kcrh-hpwan-state-of-art-03
Framework for High Performance Wide Area Network (HP-WAN)
  This document defines a framework to enable the host-network collaboration for high-speed and high-throughput data transmission, coupled with fast completion time and low latency of High Performance Wide Area Networks (HP-WAN). It focuses on key congestion control functions to facilitate host-to-network collaboration and perform rate negotiation, such as QoS policy, admission control, and traffic scheduling.
  https://datatracker.ietf.org/doc/draft-xhy-hpwan-framework/

## Slide 4
“State of Art” Updates from Last Meeting
Updates draft-kcrh-hpwan-state-of-art from v-02 to v-03:
  Improved readability with updates to key sections
  Focus on NREN R&E applications within the document, removing industrial examples.
  Clarifying architectural elements
  Inclusion of NREN/R&E examples from China
  Further discussion on emerging topics, resources, and network control
  Inclusion of additional references
Next Steps:
  We *think* the document is complete now.
  A few deep reviews would be very welcome.

## Slide 5
“Framework” Updates from Last Meeting
Updates draft-xhy-hpwan-framework from v-02 to v-03:
  adding the centralized approach for HP-WAN such as the implementation in SENSE
  adding some clarifications for the congestions for slow flow and rate fluctuations due to blind competition among multiple flows
  adding security considerations
Next Steps:
  The HP-WAN mechanisms mentioned in this framework will be implemented and simulated in Hackathon.
  We appreciate more contributions and feedbacks.

## Slide 6: Host-network Collaboration in Distributed Signaling
The host-network collaboration signaling is enabled to enhance the congestion control in HP-WAN.
  The client and server could send the traffic efficiently with the negotiated rate- based congestion control in a fine-grained way.
  The network could provide rate-based quota reservation and admission control to achieve predictable network behaviour.
  The edge node could enhance the capability to provide traffic scheduling and enforcement to mitigate incast network congestion and minimize flow completion times.
CC algrithm
Server
Transport
Transport
Transport
Transport
HP-WAN
Rate-based quato reservation and admission control
CC algrithm
CC algrithm
CC algrithm
Rate negotiation
Ingress
Edge
Egress
Edge
Transit Node
Client
Host-network Collaboration Signalling
Traffic scheduling and enforcement

## Slide 7
Host-network Collaboration in Centralized Configuration
Host-and-network collaboration could also be performed using configuration in centralized model where a controller or an orchestrator orchestrates data processing and resource allocation across hosts and network infrastructure.
  The request of scheduled traffic will be initialed to the Orchestrator.
  The Orchestrator will perform rate negotiation among hosts and networks.
  The controller of the network will perform admission control and acknowledge the traffic.
  The Acknowledgement will be configured to the client, including the response with the negotiated rate and QoS policy for the client to send traffic.
  The Controller of the network will reserve resource quota to guarantee the job's completion time.
CC algrithm
Server
Transport
Transport
Transport
Transport
Rate-based quato reservation
CC algrithm
CC algrithm
CC algrithm
Negotiated Rate
Ingress
Edge
Egress
Edge
Transit Node
Client
Traffic scheduling and enforcement
Controller
Controller
Controller
Orchestrator
Requests(traffic pattern)
Acknowledgement
Rate Negotiation
Admission Control
Acknowledgement

## Slide 8
Thanks !
Comments and suggestions are welcome.
Notes: north-south traffic需要加入一个手机，表示用户发出的